# ELECTRIC LOCKING SYSTEM EQUIPMENT

# 1	GENERAL

## 1.1	QUALIFICATIONS

The Electric Locking Systems (ELS) as specified this section is based on products manufactured by:

Dortronics Systems, Inc.

1668 Sag Harbor Turnpike

Sag Harbor, NY  11963

Tel:	(800) 906-0137

(631) 725-0505

Fax:	(631) 725-8148

Web:	www.dortronics.com

The Electric Locking Systems Contractor shall base his bid on the system hardware as specified herein.

Delete sections below if alternate products are not acceptable on this project.

Alternate techniques, modifications, or changes to any aspect of these specifications shall be submitted as a voluntary alternate.

Voluntary alternates shall be fully documented and submitted to the Owner or Owner’s representative, at least ten (10) working days prior to bid

## 1.3	RELATED SECTIONS

- Section 08110 - Steel Doors and Frames.

- Section 08210 - Wood Doors.

- Section 08300 - Special Doors.

- Section 08400 - Entrances and Storefronts.

- Section 08710 - Finish Hardware.

- Section 16000 - Special Security Control Equipment.

## 1.4	REFERENCES

Delete references from the list below that are not actually required by the text of the edited section.

- ANSI/DHI A115 Series - American National Standard Specifications for Steel Door and Frame Preparation for Hardware.

- BHMA A156.2 - American National Standard for Bored and Pre-assembled Locks and Latches.

- BHMA A156.13 - American National Standard for Mortise Locks & Latches; Builders Hardware manufacturers Association.

- BHMA A156.18 - American National Standard for Materials and Finishes.

- Certification Listings:

- Underwriters Laboratories, Inc.

- NFPA 101

- FF-H-106C - Hardware, Builders', Locks and Door Trim, General Specification for.

- The Americans with Disabilities Act of 1992.

## 1.5	SUBMITTALS

Delete any of the following paragraphs not required.

- Submit under provisions of Section 01300.

- Product Data:

- Provide manufacturer's standard details and catalog data demonstrating compliance with referenced standards.

- Provide installation instructions.

- Hardware Schedules: Submit a schedule of products specified in this section coordinated with doors and hardware specified elsewhere.

- Samples:  Submit 1 of each type of accessory device.  The Architect for installation will return approved samples on the final openings of the Project.

- Contract Close-out Submittals:

- As built schedule of locks and accessory devices.

- Operation and maintenance materials.

## 1.6	DELIVERY, STORAGE, AND HANDLING

Store products indoors in a secured area, and protect from moisture, construction traffic, and damage.

## 1.7	SYSTEM WARRANTIES

All components shall be warranted for a period of one year.  Expressed warranties are conditionally based on the requirement that the items covered within the guarantee are used and maintained in accordance with the manufacturer’s recommendations.

# PART 2	PRODUCTS

## 2.1	MANUFACTURER

Provide products by Dortronics Systems, Inc.; 1668 Sag Harbor Turnpike, Sag Harbor, NY  11963.  Telephone:  (800) 906-0137 or (631) 725-0505.  Fax:  (631) 725-4234.

## 2.3	5277 SERIES ACTUATING CONTROL DEVICES

Provide 5277-PZL Piezo button Switches as required  described below:

Switch controls shall be by Dortronics Systems, Inc. Piezo button station controls shall be Touch sensitive with no moving parts.

Operating Voltage: 12 to 24 VDC

One Normally Open Output

One Normally Closed Output

Piezo button switch life: 1 Billion Cycles

Relay life: Half Million cycles  1A @ 30VDC

Relay output contacts Rated 2A max @ 30VDC Resistive

Time delay shall be adjustable from 1 - 60 seconds selectable via an onboard Potentiometer

Relay Toggle mode ON / OFF is also selectable via Jumper setting

LED Illumination Ring is integral to the mounting plate & button. It is sealed from weather & moisture. LED Ring activates upon pressing the button to indicate change in status of the relay contacts or may be independently controlled to indicate door or lock state.

LED Illumination Status: Jumper selectable

Relay OFF: Red, Green, Yellow Or No LED Illumination.

Relay ON: Red, Green, Yellow Or No LED Illumination

LED status may also be externally controlled independent of the relay state.

Unless noted otherwise, push button switch assemblies shall be flush wall mounted to standard, recess mounted, electrical boxes, or mortise mounted into a door jamb cutout. Mounting screws will be Phillips head or flat head Pin-in-Hex tamper resistant type stainless steel as required.

Push buttons and mounting plates shall be constructed of Stainless Steel. Mounting plate is 1/8” thick with smooth edges on all four sides. A neoprene gasket is included for exterior weather resistant mounting.

Plate finish shall be Satin Stainless steel Optional text will be engraved and paint filled.

Switch Operating Environment:

Indoor & Outdoor  (meets IP-65)

Operating Temperature:

-31F to 151F

-35C to 66C

Operating Humidity: 0 to 85% (non-Condensing)

## 2.3	CONTROL DEVICE tYPE & MODEL NUMBERS

Single gang Style Button

- #W5277-PZL – 2-3/4”x 4-1/2” 1 Set NO 1 Set NC contacts with

Tricolor LED Indicator Ring Single gang Stainless Steel plate

- #W5277-PZLxE1 – 2-3/4”x 4-1/2” 1 Set NO 1 Set NC contacts with

Tricolor LED Indicator Ring Single gang Stainless Steel plate

Engraved “PUSH TO EXIT” red text

- #W5277-PZLxE3 – 2-3/4”x 4-1/2” 1 Set NO 1 Set NC contacts with

Tricolor LED Indicator Ring Single gang Stainless Steel plate

Engraved “EXIT” red text

Narrow 1-3/4” wide Mullion mount Style

- #N5277-PZL – 1-3/4”x 4-1/2” 1 Set NO 1 Set NC contacts with

Tricolor LED Indicator Ring Mullion mount Stainless Steel plate

- #N5277-PZLxE3 – 1-3/4”x 4-1/2” 1 Set NO 1 Set NC contacts with

Tricolor LED Indicator Ring Single Mullion mount Steel plate

Engraved “EXIT” red text

CUSTOM FINISHES & ENGRAVING

5277 STOCK ENGRAVING:

(SUFFIX)

xE1	ADD "PUSH TO EXIT" in Red letters (W Series only)

xE3	ADD "EXIT" in red letters

xE6	ADD for other custom engraving

5277 STANDARD HANDICAP LOGOS

xHCP	Add for blue Handicap logo

# PART 3	EXECUTION

## 3.1	INSPECTION AND APPROVAL

Upon successful completion of Electric Locking System installation, the Owner’s authorized representative shall inspect and approve the satisfactory operation of the ELS and related accessories.  Upon receipt of a detailed system adjustment list from the Owner’s authorized representative, the ELS Contractor shall complete required correction of each outstanding item on the system adjustment list.  After all items appearing on the installation/inspection report are completed, the Owner's authorized representative will make an appropriate approval.